Computers: The basic idea behind the invention of computers is the computation of numbers(data), and processing of these numbers.
 Any computer system essentially consists of :
       Processor(to carry out processing) and Memory(to store
        numbers)
In addition we also have I/O (input/output). I/O is an extended memory , it also store numbers but in a different form.
If we consider computer as a machine , I/O helps man to interact with it.
The processor nowdays are known as CPU, therefore CPU and memory are essentials.
The work of processor is to continuosly look for the data stored in memory and processing it continuosly.
Therefore in Computer Organisation the basic process is storaging and processing.

Aspects of Processor:
1. Data Path Setting: Processor is the one which is going to deal with data , so the processor must be able to setup some kind of a path to handle the data
2.Control: Apart from setting the data path processor should also be able to carry the processes through a sequence of control signals.
Components in memory:
1.Memory(closer to CPU): the one which interact with CPU directly
e.g, RAM, ROM
2.Storage(far from CPU but still effectively stores data): the one which does not interact with CPU directly
e.g, Magnetic tape , disk systems
Aspects of I/O:
1. Man-machine Interface
2. Depending upon the kind of computing system, the system may take data from the memory(data which has been already stored in the memory) or it may take data directly from I/O , which is data from the external world or real world data.
The CPU deals with I/O in same way as it deals with memory

Computer Organisation: study of computer system from programmers point of view
Computer Architecture: study of computer system from designers point of view
We can say that organisation is the study of system from software point of view whereas architecture is the study of system from hardware point of view
Application of Computer System:
1.Control Oriented Application: These are special purpose application.Here we precisely know where inputs are and we also know where our output goes .Here we have authorised user which stores a particular program in ROM (once for all can’t be replaced)
It is used for hardware application
2.Data processing Oriented Application: General purpose application, there is wide range of application.Here we don’t know about the user which stores programs in RAM (can be loaded by different users)
It is used for software application
RAM and ROM can be used in both of them

From data we further progress upto information , nowdays processors not only process data but it also storing the information and retrieving the information.
Types of processing:
1. Numeric Processing: the processing on numbers
The numeric processing basically involves arithmetic processing
2. Symbolic(text) Processing: it involves data like name ,address, etc
Symbolic Processing involves Logical Processing as these doesn’t involve no.

Now arithmetic and logical processing have come together and core of any specific CPU or processing is ALU(Arithmetic Logic Unit)
ALU is the core(essential) of any CPU

3.Graphics Processing
4. Audio Processing
5. Video Processing

- Hardware is the core of computer system and around this core various layers of software are present. Hardware is basically hard for every user to understand.Given this hardware, we are softening the particular system by providing certain features or layers,so that one need only be familiar with certain soft aspects of the system.Because of the advancement in technology more and more layers of software are present nowdays.
- The Hardware works at a very low level (machine code used earlier 0 or 1 working) , then after this we develop a layer of easiness known as assembler(A+B) and after we develop another layer known as HIGH LEVEL LANGUAGE
- Therefore we are making it easy for ourself in interacting with hard aspects of machine(hardware)
- Therefore basically software is hidding hard aspects of software